## Slide 1: Selenium Aquatic Life Criteria and Implementation
ORSANCO
Technical Committee Meeting
October 21, 2009
Holly Green, USEPA
Office of Science and Technology
Standards and Health Protection Division

## Slide 2: Today’s Discussion
Why fish tissue criteria?
What is EPA’s proposed approach to selenium chronic aquatic life criteria?
What will this mean for states and tribes?
Discussion and questions

## Slide 3: Criteria Expressed as Tissue Concentrations
Are they the wave of the future?
Not necessarily, but they have a niche.
  Most scientifically valid approach for exposure to certain pollutants
  Useful where it is important to account for site-specific factors in determining exposure (e.g., BAFs).
  Not useful for important non-bioaccumulatives such as ammonia, copper, zinc, chlorine, chloride (TDS), and most others.

## Slide 4
Fish
Primary producers
Invertebrates
Water
Toxicity to fish is better represented by a tissue value
Bioaccumulation in fish is primarily from food consumption; accumulation from water is negligible
Propensity to accumulate selenium varies widely, depending on food web and other factors.
Why a fish tissue criterion for Selenium?

## Slide 5: Fish propensity to accumulate selenium depends primarily on:
Fish diet and Invertebrate physiology
<
<
Selenium bioavailability
insects
crustaceans
bivalves
Flowing waters
Still waters
<
Selenite > Selenate
Particulate > Dissolved

## Slide 6: What is EPA’s proposed approach to chronic aquatic life criteria for selenium?
Egg-ovary concentration
Two water concentrations, derived from the egg-ovary value.
  Flowing waters
  Still waters)
Toxicological effects of selenium occur when selenium is transferred to fish eggs.
Most consistent toxic endpoint across the widest range of fish species.
The water concentration values included for ease of implementation.

## Slide 7: What will this mean for states and tribes?
Adopting both the water and egg-ovary values into WQS gives greatest flexibility in implementation.
Can use water concentration values for water quality-based effluent limits.
Can translate the egg-ovary concentration to a site-specific water concentration where desired.
Where egg-ovary concentration is available, this should be the applicable criterion, regardless of water concentration.

## Slide 8
Fish tissue
criterion
Translator
Water
concentration
Translating the selenium fish tissue criterion to a water concentration:
Relate the concentration of selenium in the eggs and ovaries of fish
to the ambient concentration in water
using the Dynamic Multi-pathway Bioaccumulation Model (DYMBAM), which incorporates organisms’ physiological characteristics and environmental conditions:
-Food ingestion rate
-Se assimilation efficiency
-Se loss rate
-Se concentration in food and water

## Slide 9
Translating the selenium fish tissue criterion
to a water concentration:
The DYMBAM adapted to translate an egg-ovary concentration
to a water concentration:
Where:
Cwater= Concentration of selenium in water (ug/L)
Cegg-ovary = Concentration of selenium in eggs/ovaries of fish (ug/g)
TTF = Trophic transfer factor: assimil. efficiency(%) X ingestion rate(g/g-d)
selenium loss rate (/d)
EF= Enrichment function(L/g): ratio of particulate to dissolved selenium in water
CF= Egg-ovary to whole body fish tissue conversion factor

## Slide 10: What implementation information will be available with the criteria?
Guidance on how to perform a site-specific translation of the egg-ovary criterion to a water concentration,
WQBEL calculations and
Recommended analytical methods.
How to provide answers to implementation questions related to monitoring, assessment and listing is still to be determined.

## Slide 11: Publication schedule
Criteria document is undergoing internal EPA review.
Draft publication expected February 2010.
Public will have the opportunity to
provide input during a 60-day period.
Final criterion is expected end of 2010.

## Slide 12
QUESTIONS?