## Slide 1: Development of Nutrient Water Quality Standards for Rivers and Streams in Ohio
Ohio EPA
ORSANCO, October 20, 2009
George Elmaraghy, P.E., Chief
Notes: <number>

## Slide 2: The Nutrient Conundrum
Define criteria for natural constituents
  Essentially asking how much is too much
    Linear dose-response model used for toxics does not apply
  Wide variations
    Many cases where nutrients are high but aquatic life is maintained, or the converse
  Indirect impacts on aquatic life
    Nutrient impacts are not direct, nutrients impact parameters such as D.O. which in turn impact aquatic life
Risk management
  Balance margin of safety without being over-protective

## Slide 3: Biological Response to Nutrients and Toxic Pollutants
Protect waters
currently achieving
Environmental Gradient
Quality of Aquatic Life
Response to Toxic
Pollutants (e.g., NH3)
Response to
Nutrient Enrichment
with “confidence intervals”
Manage to control
over-enrichment
Proactive control
for threatened waters
based on secondary
response indicators
(i.e., chlorophyll, D.O.)
Routine Monitoring
EWH
WWH
Notes: The conceptual diagram above illustrates the difference in biological response to nutrients and toxic pollutants. The curves drawn are hypothetical and should not be interpreted literally, though they generally conform to empirical evidence from several studies. The yellow shaded region depicts waters that have demonstrated biological impairment. The overlapping, grey shaded region depicts waters that are not biologically impaired, but show clear signs of over-enrichment. Management actions suggested for each region of the gradient are arrayed along the top of the graph.
<number>

## Slide 4: Stressor-response approach *
Estimate a relationship between nutrient concentrations and biological response
Relate to designated use (ideally quantitatively)
Derive nutrient concentrations protective of designated uses from the observed relationships
* Modified from “Empirical Approaches for Nutrient Criteria Derivation”
draft SAB report, 2009

## Slide 5: Approach Taken in Ohio
Empirical Approach – field assessments on small streams and rivers up to 500 sq. mi. in drainage
Concurrent chemical and biological measurements
  Biology (fish, bugs), direct connection to our designated uses
  Habitat (channel width and morphology, canopy)
  Benthic algal biomass (Chlorophyll a)
  Total inorganic nitrogen
  Total Phosphorus
  24-hour dissolved oxygen
4 years of data

## Slide 6: Effects-based Methods for Defining Nutrient Criteria
Describe relationship between nutrient concentrations and benthic chlorophyll
Linear regression
Change-point analysis
Describe relationship between benthic chlorophyll and hourly dissolved oxygen
Linear regression
Change-point analysis
Describe relationship between dissolved oxygen and fish or macroinvertebrates
Linear regression
Change-point analysis
Describe relationship between range in 24 hour D.O. and minimum D.O. at concentrations falling below WQS
Linear regression
End Result
Detected relationships & “break point values” that we can apply in the management of nutrients on a watershed scale

## Slide 7: Thresholds in Relationships Between Stressor and Response Variables Define Nutrient Criteria (all streams except nutrient sensitive streams)
Nutrients
DIN > 1.10 mg/l
TP > 0.10 mg/l
Light
Canopy > 45o open
Benthic Chlorophyll
> 194 mg/m2
24 h D.O. Range
> 7.0 mg/l
Minimum D.O.
< 5.0 mg/l
Aquatic Life
Elevated Risk of
Impairment
+

## Slide 8: Thresholds in Relationships Between Stressor and Response Variables Define Nutrient Criteria (nutrient sensitive streams)
Nutrients
DIN > 0.44 mg/l
TP > 0.04 mg/l
Light
Canopy > 45o open
Benthic Chlorophyll
> 120 mg/m2
24 h D.O. Range
> 6.0 mg/l
Minimum D.O.
< 6.0 mg/l
Aquatic Life
Elevated Risk of
Loss of Special Resource
+

## Slide 9: Application of Nutrient Criteria – Step 1 Confirm an Existing Problem or Threat
High Nutrients [> 1.10 DIN, > 0.10 TP]
Excess of Benthic Algae [> 194 mg/m2]
Wide D.O. Swings [> 7.0 mg/l]
Nutrient Impairment confirmed
[Step 2 – derive NPDES Limit or TMDL]
Is Biology Impaired or
only Marginally Attaining?
No
Yes
Step 1a

## Slide 10: Application of Nutrient Criteria – Step 1a Nutrient Sensitive Streams
Benthic Algae [< 120 mg/m2]
D.O. Swings [< 6.0 mg/l]
Minimum D.O. [> 6.0 mg/l]
Number of EPT Taxa [>15]
Nutrient Sensitive Stream
[Step 2 – permit increased N or P loads carefully]
Is the Stream Nutrient Sensitive?
No
Yes
Stop

## Slide 11: Application of Nutrient Criteria – Step 2 Implement in Management
< 1.10 mg/l DIN < 0.44 mg/l
< 0.10 mg/l TP < 0.04 mg/l
Riparian Restoration Light Riparian Protection
Protect Existing
High Quality Waters
Restore
Impaired Waters
Specifics on how to implement these criteria
are still under development

## Slide 12: Biological Response to Nutrients
Protect waters
currently achieving
TP ~ 0.04 mg/l
Environmental Gradient
Quality of Aquatic Life
Response to
Nutrient Enrichment
with “confidence intervals”
Manage to control
over-enrichment
Proactive control
for threatened waters
based on secondary
response indicators
(i.e., chlorophyll, D.O.)
Routine Monitoring
TP ~ 0.10 mg/l
EWH
WWH
Notes: The conceptual diagram above illustrates the difference in biological response to nutrients and toxic pollutants. The curves drawn are hypothetical and should not be interpreted literally, though they generally conform to empirical evidence from several studies. The yellow shaded region depicts waters that have demonstrated biological impairment. The overlapping, grey shaded region depicts waters that are not biologically impaired, but show clear signs of over-enrichment. Management actions suggested for each region of the gradient are arrayed along the top of the graph.
<number>

## Slide 13: Schedule
Small streams and rivers (< 500 sq. mi. drainage)
  Begin rule making summer 2010
  Complete rule making summer 2011
Large rivers (> 500 sq. mi. drainage)
  additional field work 2010 – 2012
  Complete rule making in 2013

## Slide 14: Contact Information
Email: george.elmaraghy@epa.state.oh.us
Phone: 614-644-2001
Fax: 614-644-2745
DSW Website: http://www.epa.ohio.gov/dsw/