## Slide 1
October 20-21,2009
Agenda Item 6a.

## Slide 2: Ohio River CSO Communities
    Pennsylvania – 10 communities
    West Virginia – 10 communities
    Ohio – 10 communities
    Kentucky – 10 communities
    Indiana – 7 communities
    Illinois – 2 communities

## Slide 4: Nine Minimum Control Status
Most of the communities are progressing toward implementation.
Max Storage is the only NMC that is not 90% implemented.
Focus now is LTCP submittal which incorporates NMC implementation.

## Slide 7: Significant CSO Community Improvements
Pennsylvania
  The PA CSO Policy’s status is finalized and the SWRO is now processing the PAG-06 General CSO permits.
Moundsville, WV
  The LTCP was approved on 12/05/08 and flow meters have been installed on all 3 CSOs.
Point Pleasant, WV
  The LTCP has been updated to an approval state. The LTCP will be approved via the permit modification process. Flow meters will be installed on both CSOs.
Louisville MSD, KY
  Total number of CSO outfalls currently is 106 which is a reduction from 113.
  Several other improvements are ongoing as stated in the Consent Decree.

## Slide 8: Significant CSO Community Improvements cont’
  Project WIN (Waterway Improvements Now) available on-line.
    Overflow Advisory Levels
    Integrated Overflow Abatement Plan
    CSO/SSO Location Maps
Paducah, KY
  Two major projects are planned which will eliminate or reduce the frequency, volume and duration of CSOs. Those projects are: (1) Paducah wastewater treatment plant upgrade – the hydraulic capacity of the WWTP will be increased from 9 to 17 MGD, allowing more wet weather flow to enter the WWTP, and (2) Perkins Creek Interceptor Separation – the scope for this project is to separate Perkins Creek Lift Station (1.5 MGD) flow from the Combined Sewer System.
  Paducah is expected to complete a design soon for a stand-by generator for its influent pump station, thus reducing bypasses during power outages.

## Slide 9: CSO Training and Webcasts
Training Courses and Meetings
  Managing Wet Weather with Green Infrastructure Workshop
    November 5, 2009-November 6, 2009-Toledo, Ohio
Training Resources-Archived Webcasts
Green Infrastructure
  The Many Benefits of Green Infrastructure & Philadelphia Case Study
  Models & Calculators and Louisville Case Study
  Retrofits: Green Streets and Operation & Maintenance
  Combined Sewer Overflows (CSO)
  CSO Control Technologies
  CSO Control Policy 101
  CSO Long Term Control Plan Basics
  More information available at: http://cfpub.epa.gov/npdes/

## Slide 10
Questions?
Please contact Stacey Cochran
At 513-231-7719 ext:124
Notes: Questions?
<number>