## Slide 1
Report of the NPDES Subcommittee

## Slide 2: Conference Call Meetings July 8 and August 19
  Mercury Discharges – Utility Request to Address Permit Requirements for Mercury in Water Discharges Resulting From Installing Air Scrubbers
  Ammonia Criteria – Proposed for Adoption to Protect Drinking Water Intakes
  Max Temperature Criteria – Once Thru NCCW at Power Plants
  ORSANCO Update – States’ Incorporation of Nutrient Monitoring Into NPDES Permits

## Slide 3: Wastewater Streams Mercury Levels
Scrubber WasteWater Treatment Plant
  Mercury up to 1 to 2 ppb
  Discharge Volume ~ 0.5 MGD
  Discharge Often Diluted by NCCW and/or Ash Ponds
FGD Landfill Leachate
  Mercury up to 100 - 200 ppt
  Discharge Volume ~ 0.2 MGD
Notes: <number>

## Slide 4: New Source: Prohibition New Load and No Mixing Zone
Annual Avg. Mercury Limit of ≤12 ppt
New Sources
  Prohibition Mixing Zone Immediately
  No New Load
Existing Sources – MZ Eliminated October 2013

## Slide 5: Mercury Discharges from Power Plants
Subcommittee Consensus
  Air Scrubbers Significantly Reduce Overall Hg Load to Environment
  Technology is “not quite there yet” to Meet 12 ppt Limit
  Some Means Needed to Provide Temporary Relief for New Source Due to Air Pollution Control

## Slide 6: Mercury Discharges from Power Plants
Power Industry Advisory Committee presented four alternatives
NPDES Subcommittee Prefers Extending Current Variance Procedure to Allow Variances to Section VI.G.
  Provides for checks and balances that the Subcommittee feels are needed.
    Site Specific – Public Review

## Slide 7: Proposed Ammonia Criterion
Pennsylvania DEP raised concerns.
  Possible impact on permit limits
  No specified design river flow
  Costs of attainment have not been quantified
Subcommittee believes modeling guidance needed – No intent trigger limits for existing discharges
  Subsequent review indicates no design flow specified for other criteria in Section IV.C.1,2, and 3.

## Slide 8: Max Temperature Criteria Once Through Cooling – Power Plants
Current temperature criteria are based on aquatic life impacts.
Narrative nuisance prevention criteria difficult to implement
Subcommittee believes a maximum temperature limit to protect human exposure should be adopted.
Pennsylvania is the only member state that currently has a guidance for such a limit.

## Slide 9: Nutrient Monitoring Requirements
Commission adopted requirements for dischargers to monitor effluents for nutrients.
These requirements are being incorporated into permits for Ohio River dischargers.
Staff will provide periodic progress reports on the incorporation of these limits.

## Slide 10: Questions????