## Slide 1: Characterization of Dissolved Solids in the Ohio River
TECHNICAL COMMITTEE
OCTOBER 8-9, 2013

## Slide 2: Background
Commission adopted 500 mg/L standard for TDS in June 2011
Rivers Users Program developed study to investigate TDS and major ions
Water Users simultaneously proposed similar study for bromide
Integrated the two study designs for cost efficiencies and more robust data set

## Slide 3: Study Objectives
Characterize ambient background levels of TDS
Quantify TDS constituent makeup to evaluate seasonal and spatial variability
Develop site-specific translators to convert conductivity to TDS
Provide data to support possible development of an Ohio River bromide stream criterion

## Slide 4: Sampling Design
Weekly samples collected at 16 sites
Collection sites located at water intakes
  Participants identified through the WUAC and PIAC
Sampling conducted for 1-year
  December, 2011 thru December 2012
Analysis – In-house and contract lab

## Slide 6: Analysis
Dissolved Solids Analytes
Sodium
Potassium
Magnesium
Calcium
Lithium
Bicarbonate
Total Dissolved Solids
Supplemental Parameters
pH
Conductivity
Temperature
Stream flow
Chloride
Sulfate
Bromide
Fluoride

## Slide 7: What do the results tell us about ambient levels of TDS?
Peak concentration in Ohio River was 368 mg/L
Median level 215 mg/L
Highest levels on Muskingum and Big Sandy Rivers
  584 mg/L and 579 mg/L respectively

## Slide 8: Are there seasonal variations?
Highest concentrations observed in late Aug./early Sept.
Stream flow is major driver of temporal variation
Concentrations of TDS and most ions are inversely correlated with Q
All OR samples well below 500 mg/L std., even during low flow

## Slide 9: What are the major ions?
5 ions makeup 93% of TDS in Ohio River
  Sulfate, bicarbonate, calcium, chloride, sodium
Bromide is typically <0.05%
  BUT, not insignificant!

## Slide 10: How does ionic composition vary spatially?
SO4 decreases from upstream to down
  36% at mile 12 to 21% at mile 978
  Beaver R. 19%; Big Sandy 42%
HCO3 doubles from 19% in Pittsburgh to 38% in Cairo
Calcium remains fairly consistent (13-16%)
Cl- shows general decline from 14.5% at mile 137 to 8.8% at mile 792
  Big Sandy 4%; Beaver R. 19%
Sodium decreases moving downstream
  11% in Pittsburgh to 7% in Cairo
Bromide generally highest in upper river

## Slide 12: What are the implications of the ion composition on the regulation of dissolved solids?
TDS standard is 500 mg/L
  Note: This study does not address appropriateness of numeric value
ORSANCO has standards for two individual ions
  Sulfate – 250 mg/L; chloride – 250 mg/L
Sulfate and chloride combined account for 43% of TDS
  Sulfate – 31%; chloride – 12%
Since the sum of the standards for SO4 and Cl are equal to the standard for TDS, it is possible to not exceed the individual ion criteria and yet have TDS levels well above 500 mg/L.
Therefore, indirectly regulating TDS through SO4 and Cl alone is not sufficient to ensure TDS levels remain below 500 mg/L.

## Slide 13: What is the relationship of TDS and conductivity in the Ohio River?
Conductivity sometimes used as surrogate for TDS
0.67 is commonly used to convert conductivity to TDS
Reported conversion factors range from 0.5 to nearly 1
  Conv. factor depends on ionic composition
Compared TDS to specific conductance
Ohio River conversion factors ranged from 0.55 to 0.58
Could overestimate TDS by 20% using 0.67 conv. factor.

## Slide 14: Comparison of Bromide to THMs
Compared THMs in finished water to bromide levels in source water
Challenges:
  Most plants only collect THM data quarterly
    Limits number of paired data sets for comparison
  Many non-detects for bromide, especially early in study period
    Further limits paired data
  Lag time between raw water sample collection and travel time through treatment plant
  Not all utilities collect THMs on plant effluent

## Slide 15: How does bromide in source water compare to TTHMs in finished water?
Bromide vs TTHMs compared across all sites
Bromide: 40 to 150 ug/L
TTHMs: 10 to 130 ug/L
No clear pattern when all sites grouped together
  Highest bromide values did not correspond to highest TTHMs

## Slide 16: How does bromide in source water compare to TTHMs in finished water?

## Slide 17: General Bromide/THM Observations
Hays Mine experienced highest TTHM levels
  No clear relationship with bromide
Wheeling’s only TTHM sample over 80 ug/L corresponded to a non-detect for bromide
Cincinnati and Cairo had very low TTHM levels, even at higher bromide concentrations
PWSA data comparison showed the strongest positive correlation between bromide and TTHMs
  Brominated THMs relative abundance greater with higher bromide levels
Large # of variables make it difficult to compare across utilities
However, many individual sites had insufficient data to discern relationship
Need more intensive monitoring to evaluate relationship between bromide and THMs.

## Slide 18: General Bromide/THM Observations
Results inconclusive to define relationship between bromide and THM formation
High bromide levels did not consistently correlate with high THM concentrations
PWSA data comparison showed the strongest correlation between bromide and TTHMs
  % brominated THMs greater with higher bromide levels
Large # of variables make it difficult to compare across utilities
However, many individual sites had insufficient data to discern relationship
Need more intensive monitoring to evaluate relationship between bromide and THMs.

## Slide 19: Comments Received
Dissolved solids report distributed to 4 committees for review and comment:
  Technical Committee
  ORSANCO/Ohio River Users Advisory Committee
  Water Users Advisory Committee
  Stream Criteria Subcommittee
Received responses from 10 individuals

## Slide 20: Summary of Comments
General comments
  Various spelling/grammatical edits
Specific conductance/TDS relationship
  Need to more clearly state recommendation regarding use of specific conductance to TDS conversion factors
Bromide
  Need to highlight data limitations in comparing bromide to THMs
  Correlation of bromide to flow by site may help differentiate natural vs man-made sources
  Correlation to TTHMs is flawed; many other contributing factors
  TDS not the right parameter to limit bromide. May need to develop bromide standard once relationship to THM formation is better understood.
  Need more site specific data to evaluate potential need for ambient water quality criterion

## Slide 21: Summary of Comments (cont)
TDS
  Should look at TDS loadings by site
  Add coefficient of variability to table of TDS results
  Did TDS result ever exceed sum of ions?
  Should mention potential impact from frack water disposal
Ion Composition
  How were the ion-specific percentages calculated?
Implications to WQ Standards
  Report is on monitoring results, not toxicity or adverse effects. Do not see how report on ambient conditions warrants revisiting a WQS.
  Do not agree with statement that stand-alone TDS standard is necessary (x2)
  Supports need for stand alone TDS standard

## Slide 22: TEC Action
Options:
  Recommend Commission approve report
  Direct staff to make revisions; bring back for consideration at February meeting