## Slide 1
Paul Novak, Ohio EPA

## Slide 2: Committee Meetings/Agenda
Committee calls on July 17 & Sept 18.
Agendas
  List of Mercury Discharges.
  Streamlined variance procedure.
  Comments on Steam Electric Guidelines
  Review of data on compliance problem discharges.
  Development of permit limits for criteria that apply at downstream intakes.
  Implementation language for human health temperature criteria.

## Slide 3: Streamlined, Coordinated Mercury Variance Procedure
Committee has been working on procedure for streamlined variance.
Originally looked at 30 ug/L as threshold for receiving variance based on IDEM process.
30 ug/L came from Michigan which they identified as having come from Maine data.
Since then Michigan reduced threshold from 30ug/L to 10ug/L, and now currently use site-specific approach which typically results in less than 10 ug/L.

## Slide 4: Possible Approach
Require low-level mercury monitoring to determine reasonable potential.
If Hg discharge < 12 ng/L as annual average (criterion is 12 ng/L) and an acceptable pollutant minimization plan has been submitted, then a streamlined variance will be granted.
Compliance schedule: 12 ng/L limit effective at end of permit
All other conditions & procedures remain as in the currently adopted procedure.
This approach in line with OEPA.

## Slide 5: List of Mercury Discharges
119 discharges with mercury monitoring requirements.
51 +/- discharges with average concentration <12 ug/L total mercury.
List has been updated and verified.

## Slide 6: Comments Submitted on EPA’s Steam Electric Guidelines
Remove options involving BPJ
  level playing field among states
  Minimizes permit appeals
Encourage EPA to set standards for FGD waste streams.
Allow for utilization of trading programs to achieve nutrient reductions.
Support proposed arsenic limits.

## Slide 7: Continuing Issues
Permitting of discharges for TDS & Ammonia that apply at downstream intakes.
Work with Power industry on development of implementation language for human health temperature criterion.

## Slide 8: TEC Consideration
Possible direction on streamlined variance procedure.