## Slide 1: Biological Condition Gradient Indiana Fish and Macroinvertebrates
Presented on October 4, 2016 to the
Ohio River Valley Water Sanitation Commission (ORSANCO) Technical Committee
By Stacey Sobat, Indiana Department of Environmental Management
Office of Water Quality, Watershed Assessment and Planning Branch

## Slide 2: Overview
What is the Biological Condition Gradient (BCG)?
  Levels of Condition
  Ecological Attributes
  Response of Taxa Occurrence to Stress
  Quantitative Model
BCG Calibration for Indiana Fish and Macroinvertebrates
  Data assemblage
  Workshop
  Decision model development and testing
  Utility to support water quality management

## Slide 3: Biological Condition Gradient
Source: Modified from
Davies and Jackson 2006
.
.

## Slide 4
Ecological Attributes Used to Characterize the BCG | 
I. Historically documented, sensitive, long-lived, or regionally endemic taxa | VI. Nonnative or intentionally introduced species
II. Highly sensitive (typically uncommon) taxa | VII. Organism condition
III. Intermediate sensitive and common taxa | VIII. Ecosystem function
IV. Taxa of intermediate tolerance | IX. Spatial and temporal extent of detrimental effects
V. Highly tolerant taxa | X. Ecosystem connectedness
Source: Modified from Davies and Jackson 2006.
Biological Condition Gradient

## Slide 5: Biological Condition Gradient
Source: Tetra Tech, Indiana Report 2016.

## Slide 6: Biological Condition Gradient
Expert judgement used with statistical approaches to develop quantitative model
Calibration by habitat type (headwater, large river) in a particular region (Corn Belt Plain, Indiana Drift Plains)
Attributes | Rules for Level 3 Some replacement of sensitive-rare species; ecosystem functions are fully maintained1 |  | Rules for Level 5 Tolerant species show increasing dominance; sensitive species are rare; functions altered1 | 
Drainage Area (square miles) | < 20 mi2 | > 20 mi2 | < 20 mi2 | > 20 mi2
Number of total taxa | ≥ 15 (10-20) | ≥ 17 (12-22) | > 2 (1-4) | > 3 (2-5)
% Attribute I+II+III+X taxa | ≥ 20% (15-25) |  |  | 
% Attribute V+VI taxa | ≤ 30% (25-35) |  | ≤ 80% (75-85) | 
1Davies and Jackson 2006 |  |  |  | 

## Slide 7: Steps in the BCG Calibration
Source: Tetra Tech, Indiana Report 2016

## Slide 8: Data Assemblage
Indiana Fish Community Data (2003-2013)
Level 3 Ecoregions
  Stream Size
Source: Tetra Tech,
Indiana Report 2016

## Slide 9: Workshop
Organization | Name
Indiana Department of Environmental Management (IDEM) | Stacey Sobat
 | Reid Morehouse
 | Paul McMurray
 | Todd Davis
 | Kevin Gaston
 | Kevin Crane
 | Ali Meils
 | Kayla Werbianskyj
 | Jim Stahl
Indiana Department of Natural Resources (IDNR) | Brant Fisher
City of Elkhart | Daragh Deegan
Muncie Sanitary District | Drew Holloway
Eastern Kentucky University | Jamie Lau
Ball State University | Mark Pyron
US Geological Survey (USGS) | Ed Dobrowolski
 | Aubrey Bunch
National Park Service (NPS) | Charlie Morris
Midwest Biodiversity Institute (MBI) | Chris Yoder
Source: Tetra Tech, Indiana Report 2016

## Slide 10: Workshop
Source: Tetra Tech, Indiana Report 2016

## Slide 11
Source: Tetra Tech, Indiana Report 2016

## Slide 12: Decision Model Development
BCG Level 2 | Large Rivers (all regions) |  | 
Number of total native taxa | ≥ 26 (21-31) |  | 
Number of Attribute I+II taxa | ≥ 1 (0-2) |  | 
Number of Attribute I+II+III+X taxa | ≥ 6 (3-9) |  | 
% Biomass Attribute I+II+III+X taxa | ≥ 40% (35-45) |  | 
Number of Attribute VI individuals | < 4 (0-7) |  | 
% DELT anomalies | 0% (0-1) |  | 
Number of minnow taxa | ≥ 2 (1-3) |  | Combination rule (applies to shaded cells) - model uses the best of 3 of 4
Number of darter + sculpin + madtom taxa | ≥ 3 (1-5) |  | 
Number of sucker taxa | > 4 (3-6) |  | 
Number of sunfish taxa | > 3 (2-5) |  | 
BCG Level 3 | Large Rivers (all regions) |  | 
Number of total native taxa | ≥ 23 (18-28) |  | 
Number of Attribute I+II+III+X taxa | > 2 (1-4) |  | 
% Biomass Attribute I+II+III+X taxa | ≥ 15% (10-20) |  | 
% Biomass Attribute V+VI taxa | ≤ 45% (40-50) |  | 
Number of individuals with DELTs | ≥ 2, flag for further evaluation |  | 
Number of minnow taxa | ≥ 2 (1-3) |  | Combination rule (applies to shaded cells) - model uses the best of 3 of 4
Number of darter + sculpin + madtom taxa | ≥ 2 (1-3) |  | 
Number of sucker taxa | ≥ 4 (2-6) |  | 
Number of sunfish taxa | ≥ 2 (1-3) |  | 
BCG Level 4 | Large Rivers (all regions) |  | 
 | alt 1 | alt 2 | 
Number of total native taxa | ≥ 16 (11-21) |  | 
Number of total individuals | -- | ≥ 95 (90-100) | 
Number of Attribute I+II+III+X taxa | > 3 (2-5) | -- | 
% Attribute V+VI individuals | ≤ 45% (40-50) |  | 
Number of individuals with DELTs | ≥ 2, flag for further evaluation |  | 
BCG Level 5 | Large Rivers (all regions) |  | 
Number of total native taxa | ≥ 8 (5-11) |  | 
Number of total individuals | ≥ 20 (15-25) |  | 
Number of individuals with DELTs | ≥ 2, flag for further evaluation |  | 
Source: Tetra Tech, Indiana Report 2016

## Slide 13: Panel Variability
Source: Tetra Tech, Indiana Report 2016
Calibration: 82% of panelist scores within 1/3 BCG Level of group median (96% 2/3 BCG Level)
Confirmation: 78% within 1/3 BCG Level (94% 2/3 BCG Level)

## Slide 14: Model Performance
Source: Tetra Tech,
Indiana Report 2016
On average, models were accurate in replicating panel assessments within ½ BCG Level:
98% for Calibration data
94% for Confirmation data

## Slide 15: Utility of Biological Condition Gradient
Additional tool to interpret natural state of the stream.
Recognize improvements along the BCG.
Identify and protect outstanding resources.
Help to prioritize resources and management actions.
Compare biological condition across the nation.
Now working on BCG for macroinvertebrates!

## Slide 16
Acknowledgements
Stacey Sobat, (317) 308-3191, ssobat@idem.IN.gov
Tetra Tech, Inc.
  Owings Mills, MD
  Jen Stamp
  Jeroen Gerritsen
  Benjamin Jessup
U.S. EPA Region 5
  Ed Hammer
Workshop Participants