## Slide 1: Bacteria Trends Report
Technical Committee Meeting
October 4-5, 2016
Agenda Item #11
Informational Item

## Slide 2: Background
Bacteria data collected routinely as part of Contact Recreation Program
Data uses:
  Weekly reporting of conditions for recreation
  Assess attainment of WQS (305b)
Municipalities spending $Billions on Long Term Control Plans and Consent Decrees
Are bacteria levels improving?

## Slide 3: Bacteria Data Availability
1990’s – Commission begins routine fecal coliform sampling
  Weekly sampling in six largest CSO communities
  May through October
2000 – Sampling sites added
  Upstream, downtown, downstream
2009 - Sites reduced to two per CSO community
2013 – Sampling period extended to include April

## Slide 4
Contact Recreation Sites

## Slide 5: Study Objectives
Evaluate observed trends in bacteria data set
  Spatial (comparison across and within CSO communities)
  Temporal (Are levels changing over time?)
  Seasonal trends
    Changes over contact recreation season
    Relationship to flow and precipitation

## Slide 6: Spatial & Temporal Trends

## Slide 12
Chart: Upstream / Downstream Comparison Fecal Coliform in Pittsburgh
| 01'-05 | 06'-10' | 11'-15'
% US exceed | 0.48765 | 0.51351 | 0.48227
% DS exceed | 0.48148 | 0.5 | 0.50355

## Slide 13
Chart: Upstream / Downstream Comparison Fecal Coliform in Cincinnati
| 01'-05 | 06'-10' | 11'-15'
% US exceed | 0.16364 | 0.12821 | 0.11043
% DS exceed | 0.27273 | 0.22436 | 0.20859

## Slide 14: Seasonal Trends

## Slide 18: Conclusions
Longitudinal
  Highest levels in Pittsburgh
  Lowest in Huntington / Cincinnati
Upstream / Downstream
  Concentrations greater at downstream site
  Exception in Pittsburgh
  Attainment improving over time (both US/DS)

## Slide 19: Conclusions (cont)
Temporal
  Highest levels in 2001 – 2005
  Slow, steady decline in subsequent 5-year periods
  Exception in Pittsburgh
    High in 1996 – 2000
    Low in 2001 – 2005
    Slight increase in subsequent 5-year periods

## Slide 20: Conclusions (cont)
Monthly
  Elevated in May
  Levels peak in June
  Steady decline from July through October
Flow
  Median concentrations steadily increase with flow
  Variability also increases with flow
Precipitation
  Median concentrations steadily increase with rainfall
  Variability also increases with rainfall

## Slide 21: Questions?