## Slide 1: AEP/EPRI Study of Speciation and Bioavailability of Mercury: Preliminary Results
Rob Reash
American Electric Power, Columbus, OH
ORSANCO Technical Committee Meeting, October 2016

## Slide 2: Basic Assumption
All (or most) of mercury is available for bioaccumulation. Thus, total Hg should be regulated.
But…..if this were true then fish tissue Hg levels should spike after high flow events.
ORSANCO water quality sampling shows the % MeHg of THg is 2 – 3%

## Slide 3: Purpose of Study
Assess the operationally-defined bioavailability of Hg in various water sample types.
Evaluate whether treated wastewater contributes to increased Hg bioavailability.

## Slide 4: Mercury in Water Samples: Typical Analyses
Total Hg (and dissolved Hg) by EPA Method 1631
MeHg by EPA Method 1630* * Assumption is that the proportion of MeHg to THg represents the bioavailable fraction of all sum mercury species.

## Slide 5: Bioavailable Hg - Not Just MeHg
Bioavailable Hg consists of two components: MeHg and inorganic bioavailable Hg (IB – Hg) that may be readily converted to MeHg. WERF, 2009 * IB – Hg also called “reactive inorganic Hg”

## Slide 6: Thus, the Fraction of Bioavailable Hg is:
f (B – Hg) = f (MeHg) + f (IB – Hg) *However, the formation and persistence of methylmercury is not always at steady state:
Hgmethylated ↔ Hgdemethylated

## Slide 7: Basic Methodology
Collection and analysis of ambient, wastewater, and mixing zone (simulated) water samples.
Analysis of THg and dissolved Hg by CV-AFS.
Analysis of MeHg by IPC-CV-ICP-MS.
Analysis of acid-labile (IB) Hg by fluorescence
Other variables that influence Hg bioavailability (TSS, TOC, pH, sulfide, sulfate, TDS).

## Slide 8: Water Sample Types
Treated wastewater: > FGD landfill leachate > FGD purge stream w/ fly ash landfill leachate > FGD purge stream w/bottom ash sluice and miscellaneous low-volume streams >FGD purge stream (from 2° clarifier)
Mixing zone > 50:50 mix of wastewater and ambient Ohio R. > Worst-case (unrealistic) mixture
Ambient Ohio River > RM 73, 241, 260

## Slide 15: Regression Analysis Results
THg vs TDS, sulfate, and conductivity: r2 = 0.40 to 0.48 (P < 0.001)
pH vs TOC: r2 = 0.20; P < 0.01
THg vs TOC: r = -0.2; NS

## Slide 16: Conclusions: Preliminary Results
Median concentrations of all Hg species were marginally higher in wastewater and mixing zone samples, however the median concentration of THg in wastewater samples was < 5 ng/L.
The median % MeHg was highest in ambient river samples, but this was < 2%.
The median % bioavailable Hg ranged from 11.3% (ambient river) to 14.1% (wastewater). Thus, the median bioavailable fraction of THg for all samples was < 20%.

## Slide 17: Recognition of the need to understand bioavailable Hg
Although THg concentration is relevant for any investigation of Hg-contaminated soils and sediments, the fraction available for methylation and, ultimately, for accumulation in the food web is of particular importance…Identification of the particular chemical species is less important than understanding the overall “available” Hg concentration.
Bighan, G.N., K.J. Murray, Y. Masue-Slowey. And E.A. Henry. In press. Biogeochemical controls on methylmercury in soils and sediments: implications for site management. Integrated Environmental Assessment and Management.

## Slide 18: Next Steps
Mercury translator study approved by Ohio EPA (James Gavin Plant BAP discharge)
Presentation at SETAC (Society of Environmental Toxicology and Chemistry) annual North American conference
Manuscript submitted to journal