## Slide 1: Current ORSANCO mercury Studies
Methyl mercury in the Ohio River
Tributary total and methyl mercury monitoring and load calculations
Upcoming: ohio river mercury total load project

## Slide 2: FY ’16 Methyl Mercury Projects
Two Site-specific MeHg BAFs under development
  Below R.C. Byrd L&D, Mile 282
  Below Newburgh L&D, Mile 782
24 Additional Ohio river mercury and methyl mercury analyses

## Slide 3: Ohio River Methyl Mercury characteristics
69 Paired measurement include USGS Cooperative, FGD Study Raw Intake, and three baf studies

## Slide 4: Ohio River Methyl Mercury characteristics
Valid detections of 3.5% Methyl mercury occur infrequently

## Slide 5: The Shape of Ohio River Methyl Mercury data
the median percent methyl mercury 1.5% of Total mercury River-wide

## Slide 6: The Shape of Ohio River Methyl Mercury data
Occurrences of higher percent methyl happen in all ohio river locations

## Slide 7: The Shape of Ohio River Methyl Mercury data
Seasonal pattern emerging
“methyl mercury is 1.5% of total mercury”

## Slide 8: Tributary Mercury and Methyl Mercury Monitoring
15 Major tributaries
84% of Ohio River drainage
165 of 180 events complete

## Slide 9: 6 Months of Tributary Monitoring (N=90)

## Slide 10: Percent methyl Mercury Differences (N=90)

## Slide 11: Tributary mercury Monitoring
Project Goals:
  Daily Loads/Annual Loads
  Average yields (mass/drainage area)
  methylation efficiencies

## Slide 12: Load calculation: 12 Monthly Samples
Sample events ranged from 88th to 4th percentile flows

## Slide 13: Total Hg vs Flow Regressions
12 Monthly Events
83% Correlation
p-value <0.0001

## Slide 14: Tributary Flow Regressions after 6 months

## Slide 15: FY ‘17 Total Mercury Load Project
Planned start in November 2016
Use Previously Calculated Tributary loads
  indicate Direct deposition and discharge load to the Ohio River
Project planned near smithland lock and dam
  Location with highest mercury concentrations in fish tissue
  Upstream of the Cumberland and Tennessee rivers