## Slide 1: HAB Event
Agenda Item 10c

## Slide 2: Timeline
Began Aug 19 as a NRC reported paint spill at ORM 84 (Wheeling, WV)
  Identified as Microcystis Aerugenosa
Aug 21 ORSANCO sampled from ORM 65-94. All toxin results below advisory limits
  OEPA sampled at Sunfish Creek. Toxin concentration 41 ug/L
Aug 26-27 ORSANCO sampled from ORM 55-126
  Toxin concentration as high as 630 ug/L at ORM 115
  Microcystis Aerugenosa cell counts up to 31,000,000 cells/ml
  Visual observation of bloom to ORM 161
Aug 28 COE reported bloom at Belleville (ORM 204), Racine (ORM 237), RC Byrd (ORM 279), and Greenup L&D’s (ORM 341)

## Slide 3: Timeline
Week of 9/1: First indication of bloom in Meldahl and Markland Pools (Cincinnati area)
Week of 9/7: Bloom extends to Indiana. Survey of McAlpine pool finds bloom nearly to Louisville, KY (ORM 606) although toxin concentrations were below advisory threshold
Week of 9/14: Bloom extended throughout the McAlpine pool.

## Slide 4: Timeline
Week of 9/21: Survey identifies bloom down to Cannelton L&D (ORM 720). Toxin concentrations below 10 ug/L through out the pool.
Week of 9/28: Report of localized algae near Evansville Water (ORM 791). Sampling in the area identified algae at Cannelton but not below.
The bloom is still on-going.

## Slide 5: Sampling Efforts
ORSANCO sampling crews conducted 14 surveys. Focus was on extent.
PA, WV, OH, KY, IL all had crews sampling sections of the river and their tributaries
US EPA and Corps of Engineers provided sampling crews
Aerial Surveys:
  WV DEP – 2 from Huntington to Sistersville
  OEPA – 1 survey from Cincinnati to Marietta
  Corps of Engineers- 1 survey from Hannibal to JT Myers
  NASA – 2 surveys with hyperspectral imaging

## Slide 6: Where To Sample?

## Slide 7: Sample Results

## Slide 8: Aerial Survey Results

## Slide 9: Advisories

## Slide 10: Coordination and Communication
ORSANCO has coordinated response with 6 States, 6 Federal Agencies (USEPA, Corps, F&W, USGS, USCG, NASA), numerous local health departments
Weekly conference calls
Distribution of survey results
Twice weekly updates to Commissioners

## Slide 11: HAB Monitoring and Response Plan
Communication was the most challenging aspect.
  ORSANCO communicated with State permitting and health departments
  State responsible for communication to local health departments
How do you sample weekly when the bloom covers 700 miles?
When is the bloom over?
Communications: If analytical reports indicate the presence of algal toxins ORSANCO will inform the States and Ohio River water utilities. ORSANCO will coordinate with the States to report the conditions to the local health departments.
Actions: Toxin analysis will continue weekly until the HAB abates

## Slide 12: Discussion Points
When is it over?
Better and easier Communication/Data Collection/Distribution
  Sharepoint
  What to do with provisional or confidential data?
What is the cost of the HAB?
  Water utilities increased PAC
  Intake closures
  River events cancelled
Monitoring Parameters
  Improved understanding

## Slide 13: Outputs
After Action report
HAB Monitoring and Response Plan update
Causes
Others?

## Slide 14: Summer 2015 Monthly Precipitation Relative to Normal
May
June
July
August
September

## Slide 15: Role of Tributaries
Muskingum River
Wabash River