## Slide 1
Marcia Willhite
Illinois EPA
ORSANCO Tech Committee
October 2011
Notes: <number>

## Slide 2
Public Water Supplies (nitrate) - 83 miles not supporting - 3 lakes not supporting - 8% of community water supplies have elevated nitrate
Aquatic Life - Phosphorus a contributing cause in 35% of impaired stream miles

## Slide 3
Of lake acres impaired for aesthetic use - 82% impaired in part by total P - 81% impaired in part by aquatic algae
30 River/Stream segments impaired in part by aquatic algae
Illinois is one of the largest contributors of nutrients to the Gulf of Mexico ∙ 15 - 19% of total N load ∙ 10 – 13% of total P load

## Slide 4
Sources Contributing to Gulf
Statewide
Nitrogen Load Phosphorus Load
Sewage effluent 16% 47%
Non-point 84% 53% (primarily agriculture)
Urban stormwater important, not well quantified
<number>

## Slide 5
Phosphorus Effluent Standard – 1 mg/L P for new/expanded discharges
Anti-degradation – required evaluation has resulted in P and/or N limits
TMDLs for nitrate and P – WLA has resulted in permit limits
USEPA letter to limit nutrients to address narrative standard – only approach under existing regulations is TMDLs – considering revised narrative
Considering technology-based requirement triggered by impairments or facility upgrade.

## Slide 6
<number>

## Slide 7
<number>

## Slide 8
<number>

## Slide 9
Algae and aquatic plant growth of unnatural origin is prohibited
The regulation was changed in 1990 striking aquatic life use protection language
Regulation contains no hint as to what is unnatural
<number>

## Slide 10
The presence of algae or aquatic plants in a water body will be considered an offensive condition with regard to aquatic life use, and could be termed cultural eutrophication, when in any 24 hour period, both of the following conditions occur:
  the dissolved oxygen water quality standard of Section 302.206(b)(1)(A), 302.206(b)(2)(A), 302.206(c)(1)(A) or 302.206(c)(2)(A) is not achieved, and,
  dissolved oxygen exceeds 100% saturation.
<number>

## Slide 11
Using this pattern of algae impact as the guiding principle of determining when too much phosphorus is present has advantages:
  Grounded in the DO WQS
  Easily measured
  Directly in the cause/effect chain
Excess Phosphorus Excess Algae Low DO = Eutrophication
<number>

## Slide 12
<number>
Notes: <number>

## Slide 13
Facilities currently causing or contributing to excess algae/plant growth are given technology-based phosphorus limits regardless of expansion/renovation plans
Decision based on violation of the narrative WQS
Difficulties anticipated in determining what facilities are significant contributors to downstream excess algae growth
<number>

## Slide 14
Any effluents from new or expanded treatment works, or from treatment works that have undergone replacement or upgrade of facilities without increasing design average flow when such improvements total 50% or greater of the net worth of the treatment works, shall meet the following phosphorus concentrations:
<number>

## Slide 15
Phosphorus limits are triggered when a treatment plant expands or otherwise is in a building mode.
Phosphorus limits depend on the size of the treatment plant.
  Reasonable/affordable technology to be determined by ongoing engineering studies
  Smaller plants will have no limit
<number>

## Slide 16
No clear cause-effect relationship allowing numeric WQS
  Other factors drive algae/plant growth in IL streams
Technology-based limits are proactive
Technology-based limits get directly to what can be done to reduce phosphorus
  Regulating ~10% of facilities addresses ~90% of P
Technology-based limits allow financial planning
Unmanageable WQBELs are avoided
<number>

## Slide 17
45% of P in IL streams is from point sources
55% of P in IL streams is from non-point sources
  Dr. Mark David, U of IL
90% of point source flow will be covered under technology limits
  If average reduction is from 3.5 mg/L to 1.0 mg/L P
Then ~ 64% of the point source P is removed
Therefore, ~29% of total stream P is removed
<number>

## Slide 18
Watershed | Target Nutrient
Lake Bloomington | Total Phosphorus Nitrate
Lake Vermilion | Total Phosphorus Nitrate
Lake Decatur | Total Phosphorus Nitrate
Vermilion River (Illinois Basin) | Nitrate
Salt Fork Vermilion River (Wabash Basin) | Nitrate
Lake Mauvaise Terre | Total Phosphorus Nitrate
Illinois Priority Watersheds to Reduce Nutrient Loss
<number>

## Slide 19
<number>

## Slide 20
Project | Description
Mississippi River Basin Initiative (MRBI) – Indian Creek Watershed | Targeting implementation activities on a small watershed. Focused on nitrogen input to PWS river. Weekly sampling during spring and summer, monthly the rest of the year. Beginning an edge of field monitoring program - CIG
Vermilion Watershed | Using edge of field BMPs to reduce nitrogen inputs
Big Bureau Creek | Recently designated as MRBI

## Slide 21
The Grove at Kickapoo | Stream naturalization, wetland and floodplain restoration, two stage ditch. With control/non-control, upstream/downstream monitoring, includes nitrate probes for continuous monitoring. Part of USEPA national NPS monitoring program

## Slide 22
Load Reduction Strategy | An implementation activity for TMDLs whereby a total load allocation for nutrients (and other pollutants w/out standards) is developed along with an implementation plan. (TP TMDLs still developed for lakes impaired by TP). There are six completed LRSs and 3 on-going.
Lake Bloomington Nitrate Reduction Program | BMP study for nitrate reduction, completion of wetlands, bio-reactor, cover crops. Some monitoring, partnering w/Blm and TNC

## Slide 23
P standards 0.05 mg/L for lakes greater than 20 acres (aquatic life)
Nitrate standard 10mg/L for public water supplies
Continuing to work on identifying NNC for flowing waters (aquatic life)
Exploring a protective standard for low P streams/rivers