## Slide 1: Why ORSANCO’s Recreational Use Criteria Should be Updated in October 2012
ORSANCO POTW Advisory Committee
Presentation to ORSANCO’s Technical Committee
October 11-12, 2011
Washington, DC

## Slide 2: What are we recommending?
Adopt new recreational uses in October 2012
  Focus on E. coli
  Recreation season geometric mean
  Change “single-sample” maximum to a statistical threshold value of 25%
  Temporary use suspension for the Ohio River (based on stage/flow when conditions are unsafe)
Notes: When ORSANCO adopted EPA’s 1986 E. coli bacteria criteria, the geometric mean was applied across a 30-day period and ORSANCO chose to interpret the 236 colony forming units per 100 milliliters as a value that was never to be exceeded.
EPA has clarified that the geometric mean can be applied across the entire recreation season and that the single sample maximum was not supposed to be interpreted as a never-to-be-exceeded criteria.
These two conditions make the criteria more conservative than they were intended.
EPA’s current thinking is that selecting the 25th percentile of the beach data would be protective. This would mean that 25 percent of the recreation season values could exceed 235, and the river would be considered in attainment of the recreational use.
For reasons that I will explain later, we also believe that it does not make sense to try to spend scarce resources on implementation strategies that would protect recreational uses when the river is not safe for swimming. This is why we are recommending that ORSANCO consider adopting a temporary use suspension under extreme high stage/flow conditions.
<number>

## Slide 3: Our Perspective on EPA’s Current Thinking on Recreational Use Criteria
Commend EPA’s efforts to develop new recreational use criteria for coastal waters & Great Lakes beaches
Support their efforts to make the 1986 criteria consistent with today’s understanding of past and present epidemiological-microbiological studies
Recognize a need to help EPA evaluate options for inland waters
  Differences between a beach on a lake and a flowing river
Notes: POTWs commend EPA’s efforts to develop new recreational use criteria for coastal waters & Great Lakes beaches.
And we support EPA’s efforts to make the 1986 criteria consistent with today’s understanding of past and present epidemiological-microbiological studies.
However, we recognize a need to help EPA evaluate options for inland waters.
The photos compare a lake beach and the Ohio River. The Ohio River is different than a beach and the uses are different.
We think that applying the 1986 criteria to the river when it is not safe for recreation is not appropriate.
<number>

## Slide 4
ORSANCO, POTWs, and EPA have all made investments. We now have:
  Improved water quality
  Information on how people use the river for recreation
  More data and understanding of cost-effectiveness of controls
  A better educated public
Our proposal is consistent with current science
We need to spend money to protect recreational uses when, and only when, they can be safely achieved

## Slide 5: Why Update ORSANCO’s Standards?(2)
Large Capital Programs
CSO/SSO Consent Decrees
Municipal Separate Storm Sewer Systems (MS4s)
  Green infrastructure
Total Maximum Daily Loads (TMDLs) for
  980-miles of Ohio River
  31,000+ miles of tributaries in 8 states
Future needs
We Need a Standard that Promotes
Innovation
  To use cost-effective technologies
Prioritization
  To spend money on controls that provide the most public benefit
Integration
  Example: green infrastructure focuses on controlling the smaller storm events

## Slide 6: Bacteria Data Near Pittsburgh
EPA. 2010. Ohio River Bacteria TMDL Development: Summary of Data Analysis and Conceptual Model Development. August 2010.
Notes: Here is an example of what I am talking about, which is a “load-duration” curve that EPA constructed as part of the work on the Ohio River bacteria TMDL.
The figure is a plot of fecal coliform data near Pittsburgh from 1992 to 2005. The bacteria levels (on the vertical axis) are plotted against the flow conditions (on the horizontal axis). All the data above the red line, are greater than 400 fecal coliform, and if this were the target for the TMDL, controls would have to be implemented that would be effective at reducing the bacteria across all of the flow conditions, including the very high flows on the left and the lower flows on the right.
The photographs on the bottom show what different portions of the river look like under the different flow conditions.
So I ask you, does it make sense to have a single E. coli value that has to be met under all flow conditions?
<number>

## Slide 7
There are 31,152 miles of tributaries to the Ohio River in ORSANCO’s 8 member states and 50 communities along the mainstem.
Notes: This is a map of the Ohio River basin for the 8 member states. The communities in yellow are the communities along the 980 miles of the Ohio River that have to spend hundreds of millions or even billions to comply with federal or state consent orders to control combined sewer overflows. These same communities are going to have to eventually spend money to control nutrients that are contributing to problems in the Gulf of Mexico and other emerging contaminants like those from personal care products. If we spend all of our money trying to eliminate bacteria under all flow conditions, there will not be enough money left.
Further, a single-sample maximum criteria means that local TMDLs will have to be done for all of the tributaries discharging to the mainstem river. There are over 31,000 miles of tributaries in the 8 member states in the Ohio River basin.
<number>

## Slide 8: Why do POTWs Care?
We have spent, and continue to spend, billions to control sewer overflows
  Implementing controls, sometimes with partners
  Costs projected to exceed $10 billion for 8 utilities
  One community expects total program cost could exceed $4 billion
We need to spend money wisely so there is money left for future costs
  Failing infrastructure, MS4, nutrient removal, emerging contaminants
Political pressure associated with increased rates
  Average of 15 percent per year
  One community’s rates have increased by 264 percent!
  Every dollar spent needs to have demonstrated public health and environmental benefits
  Fiduciary responsibility to customers
Notes: <number>

## Slide 9: Tools to Help Make these Changes
Public education
Stakeholder groups
Watershed characterization and linking sources with water quality impacts
  Monitoring data
  Collection system models
  Watershed & water quality models
Developing recreational use tools

## Slide 10: Tough Choices and Changes
Conditions demand change
  Cities laying off police and firefighters
  Increased spending on those in need
  CWA compliance costs have sky-rocketed and are largely borne by local governments
  Pullback of air regulations by the federal government
Local initiatives
  “Perfect Storm” CSO Communities Summit in Cincinnati
  Legislation in Kentucky and Ohio on CWA issues
US Conference of Mayors’ initiatives
  Dialog with EPA/DOJ headquarters on CSO/SSO Consent Decrees
  Dialog with EPA on integration of wastewater, stormwater, and drinking water programs linked with cost/benefit and affordability

## Slide 11: Justification for Change
ORSANCO’s standards are not consistent with EPA clarifications on how the existing criteria should be applied or their current thinking on new criteria
EPA’s new criteria have been developed for Great Lakes and coastal waters’ beaches
  But, EPA intends to also publish them for inland waters
  Lock and dam operation on the Ohio
Ohio River recreational uses are less frequent and different

## Slide 12: Why October 2012?
Cost and education has created public support
Utilities committed to continue to make improvements and educating public on need to do so
New science supports the changes
Regulations need to allow for fiscally-responsible solutions
Programs can’t afford to wait another three years

## Slide 13: Closing
Position statement provided to the Commissioners
POTW Advisory Committee to develop white paper on changes and justification
  Draft in late December 2011
  Final for February 2012 Commission meetings

## Slide 14: Thank You!
Contact Information
Mike Apgar
  Chairman, ORSANCO POTW Advisory Committee
  Director of Governmental Affairs
  Sanitation District No. 1 of Northern Kentucky
  Ft. Wright, KY
  (859) 578-7457
  mapgar@sd1.org
POTW Advisory Committee
ALCOSAN
City of Henderson,
City of Huntington, WV
City of Owensburg, KY
City of Parkersburg, WV
City of Portsmouth, OH
City of Steubenville, OH
Louisville Jefferson County Metropolitan Sewer District
Metropolitan Sewer District of Greater Cincinnati
Sanitation District No. 1 of Northern Kentucky