## Slide 1: Pollution Control Standards Issues: Mercury
187th Technical Committee Meeting
October 11-12, 2011
Washington, DC
Notes: <number>

## Slide 2: Mercury Issue
Aquatic Life Criteria (total recoverable):
  0.91 ug/L chronic; 1.7 ug/L acute.
Dual Human Health Criteria:
  0.012 ug/L total recoverable mercury in water.
  0.3 mg/Kg MeHg in fish tissue.
Is a water column criterion necessary?
Is the current water column criterion correct?

## Slide 3: Water Quality Violations: Total Hg

## Slide 4
2010 Methylmercury Fish Tissue Data

## Slide 5: Comparison of AWQC for Mercury
 | Aquatic Life |  | Human Health | 
 | Acute | Chronic | Water, ng/L | Fish Tissue, mg/Kg
U.S. EPA | 1,400 d | 770 d | -- | 0.3 MeHg
ORSANCO | 1,700 t 1,445 d | 910 t 774 d | 12 t | 0.3 MeHg
ILLINOIS | 2,200 d | 1,100 d | 12 d | --
INDIANA | 2,400 t | 12 t (at POW) | 140 t | --
KENTUCKY | 1,400 t | 770 t | 51 t | 0.3 MeHg
OHIO | 1,700 t 1,400 d | 910 t 770 d | 12 t | --
PENNSYLVANIA | 1,400 t 1,190 d | 770 t 655 d | 50 t | --
WEST VIRGINIA | 2,400 t | 12 t MeHg | 140 t | 0.5 MeHg

## Slide 6: 2010 305b Issues
Exceedances of fish tissue criterion were primarily for total mercury in large stripped bass populations.
Striped bass represents worst-case and not representative of typical consumption patterns.
Most total mercury exceedances were at concentrations not far above methyl criterion.
New ORSANCO study of total & methyl was indicating lower percentages of methyl in fish.
CONFLICTING DATA SETS!!!!

## Slide 7: Workgroup Recommendation
Use EPA’s 2010 Guidance for Implementing the January 2001 Methylmercury Water Quality Criterion

## Slide 8: 2010 Guidance for Implementing the January 2001 Methylmercury Water Quality Criterion
Option 1: Implement fish tissue criterion without a water column criterion.
Option 2: Translate fish tissue criterion to a water column criterion.

## Slide 9: Option 1
Implement the fish tissue criterion without the water column criterion.
  1) Determine reasonable potential of discharge.
  2) Determine status of attainment of fish tissue criterion.
  3) Implement mercury minimization plan & discharge monitoring.
  Not the most practical approach for Ohio River due to number of discharges, total loading & number of tissue samples exceeding criterion.

## Slide 10: Option 2
Translate tissue criterion to water column criterion.
  Develop site-specific BAFs.
  Modelled BAFs.
    Require as much data as site-specific approach
  Use BAFs that are not site-specific.
Best approach is development of site-specific BAFs.

## Slide 11: Site-specific BAFs
BAF = Cw / Ct.
Ohio River methylmercury BAF Demonstration Project
  One site
  Monthly water X-sectional samples for one year.
  8 tissue samples of commonly consumed fish across trophic levels 2,3 &4.
  All samples analyzed for total & methyl mercury.
  $39K direct costs.