## Slide 1
305b report

## Slide 2
Draft assessments provided to states’ 305b Coordinators by year-end.
  Use the most current data possible.
  All data used in assessments not yet available.
  BacT, fish tissue & biological assessments.
TEC signs off on assessments at Feb meeting.
Draft report completed for June TEC mtg.

## Slide 3
Conflicting data sets involving:
  Iron water violations of AL criteria vs. biological assessments using fish index.
  Mercury water violations vs. fish tissue violations.
TEC action at last meeting directing staff to utilize weight of evidence approach in 2012 assessment.

## Slide 4
Mile Point | SiteName | Criteria | Total Samples Jul '06-Jul '10 | WQC Violations | % Violations | Assessment
11.8 | Sewickley* | 1500 ug/L | 19 | 4 | 21% | Partial Support
42.6 | E. Liverpool* | 1500 ug/L | 9 | 1 | 11% | Partial Support
54.4 | New Cumberland | 1500 ug/L | 24 | 1 | 4% | Full Support
84.2 | Pike Island | 1500 ug/L | 24 | 3 | 13% | Partial Support
126.4 | Hannibal | 1500 ug/L | 24 | 2 | 8% | Full Support
161.8 | Willow Island | 1500 ug/L | 24 | 2 | 8% | Full Support
203.9 | Belleville | 1500 ug/L | 23 | 4 | 17% | Partial Support
279.2 | R.C. Byrd | 1500 ug/L | 27 | 2 | 7% | Full Support
341 | Greenup | 3500 ug/L | 31 | 2 | 6% | Full Support
477.5 | Anderson Ferry | 3500 ug/L | 24 | 2 | 8% | Full Support
531.5 | Markland | 2340 ug/L | 24 | 2 | 8% | Full Support
600.6 | Louisville | 2340 ug/L | 24 | 6 | 25% | Not Supporting
606.8 | McAlpine | 3500 ug/L | 1 | 1 | 100% | Not Supporting
625.9 | West Point | 2340 ug/L | 25 | 9 | 36% | Not Supporting
720.7 | Cannelton | 2340 ug/L | 33 | 10 | 30% | Not Supporting
776 | Newburgh | 2340 ug/L | 25 | 8 | 32% | Not Supporting
846 | J.T. Myers | 2340 ug/L | 24 | 9 | 38% | Not Supporting
918.5 | Smithland | 3500 ug/L | 24 | 4 | 17% | Partial Support
939.9 | L&D 52 | 3500 ug/L | 24 | 7 | 29% | Not Supporting
* PADEP data |  |  |  |  |  | 

## Slide 7
2010 Methylmercury Fish Tissue Data