## Slide 1: Pollution Control Standards
1) Proposed 2012 PCS Revisions
2) Draft Variance Process
3) Consideration of PPG Variance Request
4) Potential Future Variance Requests
Note: Report of the PCS Committee attached to Commission Meeting agenda.

## Slide 2: Proposed 2012 Revisions to ORSANCO Pollution Control Standards

## Slide 3: Issues Under Consideration
1) Reorganization of standards document to enhance its usability.
Temperature criteria for aquatic life revised.
Temperature criterion for human health added.
Selenium criteria revised.
Contact Recreation Criteria revised.
Variance section revised.

## Slide 4: Document Reorganization Content of 2011 Standards
Authority and Purpose
Definitions
Designated Uses
Water Quality Criteria
Waste Water Discharge Requirements
Mixing Zone Designation
Limitation
Variance
Analytical Methods
Severability Clause
Appendices

## Slide 5: Content of Proposed 2012 Standards
Chapter 1: General Provisions
  Authority & Purpose
  Definitions
  General Conditions
  Limitations
  Severability
  Variances
  Site Specific Criteria
Chapter 2: Designated Uses
Chapter 3: Water Quality Criteria
  Summary Table of Criteria (Added)
  Aquatic Life
  Human Health
Chapter 4: Mixing Zones
Chapter 5: Wastewater Discharge Requirements

## Slide 6: Temperature Criteria for Aquatic Life Protection
Proposed revisions were based on more recent scientific data on temperature endpoints for aquatic life (Upper lethal value for Spotted Sucker) and more recent ambient temp data for the Ohio River.
Proposed revisions were to change from 89 deg F to 87.8 deg F.
Received Public Comment after Close of Comment Period
  Upper lethal value reported as >89 deg F in literature.
  However, 89 deg F was used in the criteria development model.
  Comments received from Temp Workgroup were in favor of not including revised.
Recommended revisions based on ambient temperature data developed by temperature work group remain.

## Slide 9: Temperature Criterion for Human Health Protection
To protect human health from exposure to contact with water; to prevent burns.
Maximum temperature of 110 deg F.
Applies everywhere: inside and outside the mixing zone.
Temperature workgroup recommended 116.5 deg F.

## Slide 10
American Burn Association – Scald Injury Educator’s Guide
  5 min exposure to 120 = adult 3rd degree burn
  Children have thinner skin & less surface area
PADEP
  Public safety value = 110
WHO
  Hot tub temperatures should be <104
  = prolonged exposure (15-20 min)
Antiscald Inc (based on Moritz & Henriques 1947)
  120 = 2nd degree burn in 8 min
    Pub says 9 min 30 sec to 2nd degree burn at 120.2 degrees
  118.4 = 2nd degree burn in 15 min
  116.6 = 2nd degree burn in 20 min (25 according to original pub)
  113 = 2nd degree burn in 2 hours
Diller 2006
  Reduce temp standards by 3-4 degrees to apply to children
Huyer et al 1997
  108-113 = “too hot for activities; threshold for sensation of pain in adults”

## Slide 11: Recreational Use Criteria
1) Recreation season extended from May-Oct to Apr-Oct.
2) Revisions based on USEPA’s proposed criteria:
  a) Fecal coliform criteria removed from Chapters 3 & 5.
  b) Monthly geometric mean E. coli criterion of 130/100mL revised to 90-day geometric mean criterion.
  c) Single sample monthly max E. coli criterion of 240/100mL revised to not to be exceeded in more than 25% of samples in 90 day period.

## Slide 12: Comparison of Proposed Revisions
 | # Mos. Exceed | % Mos. Exceed | Assessment
ORM 462.5 | 3 | 10% | Full Support
ORM 477.5 | 11 | 37% | Non-Support
 | # Mos. Exceed | % Mos. Exceed | Assessment
ORM 462.5 | 1 | 5% | Full Support
ORM 477.5 | 3 | 15% | Partial Support
30-Day Geo Mean E. coli 130/100mL
90-Day Geo Mean E. coli 130/100mL
Maximum Criterion E. coli 240/100 mL
Current single sample max criterion not exceeded in > 10% of all samples.
Proposed 25% in 90 days: Allows 3 exceedances in any 90 day period.

## Slide 13: Selenium Criteria
Current Selenium Criteria are considered outdated.
States have been reluctant to delete criteria without replacement.
US EPA is said to be close to issuing new criteria.
Acute aquatic life criterion of 20 ug/L removed while the chronic aquatic life criterion of 5 ug/L has been retained.

## Slide 14: Revisions to Variance Section
1) Removed provision requiring concurrence from all affected states that a variance would be considered.
2) Added a statement that ORSANCO would seek the state’s regulations that would allow the requested variance to be implemented (intended to be done prior to evaluating a variance application).
Added a provision that approved variances would become part of the standards.
Note: This would require conducting the full standards revision process.
4) Variance not to exceed 5 yrs (instead of permit expiration).

## Slide 15: PCS Review Process
Public Comment Period Opened May 11, 2012.
  Several hundred postcards.
  Several thousand emails.
  Public notice to newspapers basin-wide.
Webinars held May 24, 2-4PM & May 30, 6-8PM.
Hearing June 19, 2012, 4-7PM, Cincinnati Airport Holiday Inn.
Comment period closes July 20, 2012.
Commission Action on Proposed Revisions October 11, 2012.

## Slide 16: Public Comments Received
2 Dozen Comments Received
20 comments concerned about revisions to contact recreation criteria, selenium, and variance language. Support temperature revisions & addition of April to recreation season.
Ohio Utility Group concerned about addition of temperature criterion for human health & Commission authority to grant variances. Support selenium revisions & AL temp criteria.
POTW supports revisions to contact recreation.
KY Chamber supports selenium revisions.

## Slide 17: PPG Variance Request
Made public notification within 30-days of receipt of PPG’s request.
Initial information submittal and two subsequent submittals from ORSANCO’s info requests.
Site visit with WVDEP made.
All info on ORSANCO’s website.

## Slide 18: Standards Committee Recommending Commission Approval of PPG Variance
Would allow mixing zone for mercury.
Made public notification and opened 30-day public comment period.

## Slide 19: Specifics of Proposed Approval
1) Variance not to exceed 5 yrs beginning Oct 16, 2013.
2) Monthly avg limit not to exceed 55 ng/L.
3) Commission’s criteria must be met outside mixing zone.
4) WVDEP may establish daily max limits.
5) Mercury reduction plan must be fully implemented.

## Slide 20: Specifics (cont.)
6) Annual progress reports required.
7) Monthly Ohio River instream & annual fish tissue monitoring required to demonstrate compliance with standards.
8) Commission shall have sole authority to modify, renew or revoke the variance.
9) Variance would not limit WVDEP’s authority to impose additional or more stringent requirements.

## Slide 21: Public Comments
116 comments in favor of granting variance, 89 opposed.
Responsiveness summary in agenda package.
Revisions based on comments to include fish tissue monitoring.

## Slide 22: Variance Application & Review Process
PCS Committee is recommending:
  1) Draft be followed for all requests until finalized.
  2) Draft be finalized after completing the first variance request.
  3) Initially no application fees but continue to monitor workload.
  4) Generic process will apply to all variance requests.
  5) Approved variances adopted into standards.

## Slide 23: Public Process
1) Public notification within 30 days of receipt of variance application.
2) PCS Committee evaluation & recommendation to Commission.
3) Commission authorization for 30-day public comment period.
4) Commission consideration at next meeting.
5) Standards adopted into standards if approved.

## Slide 24: Approval Criteria
1) Demonstrate cannot meet standards without mixing zone.
2) Demonstrate there are no reasonable alternatives.
3) Submission of an adequate Pollution Minimization Plan.
4) Identification of best effluent quality achievable.
5) Demonstration that best achievable effluent quality will meet standards outside mixing zone.

## Slide 25: Future Variance Requests
City of Ironton, OH WWTP won’t be able to meet mercury criterion without mixing zone.
  OEPA draft permit includes language that they must make request to ORSANCO.
  We have not received a request.
SABIC in Indiana has talked with us but has not made a formal request.

## Slide 26: Questions?