## Slide 1: Contact Recreation Monitoring
The Commission collects bacteria samples from May through October in six large urban communities with combined sewer systems to evaluate support of the contact recreation use. We currently collect a sample at an upstream and downstream location in Pittsburgh, Wheeling, Huntington, Cincinnati, Louisville, and Evansville. Five rounds of sampling are completed monthly for each urban community sampling location and analyzed for fecal coliform and E. coli using Membrane Filtration. Those five samples are then used to produce a monthly Geometric Mean which is 240CFU/100mL for fecal coliform and 130CFU/100mL for E.coli. In Cincinnati we also analyze for Enterococci using Enterolert and analyze for E.coli using Colilert in-house at four extra sites. ORSANCO has also helped in some special projects this year including Buffalo Trails Multisport Racing (Maysville), Louisville Triathlon, Ironman (Louisville), The Great Ohio River Swim and Cincinnati Triathlon.

## Slide 3: Dissolved Oxygen and Temperature Monitoring
Dissolved oxygen and temperature is monitored by the United States Army Corp of Engineers, electric utility/hydropower agencies or ORSANCO at 9 Ohio River stations. These stations are monitored in hourly, 30-minute or 15-minute increments to obtain temperature and dissolved oxygen data for the assessment of aquatic life water quality criteria. The average D.O. concentration shall be at least 5.0mg/L for each calendar day. The allowable temperature varies each month and Period Averages range from 68°-82°F.
Station | River Mile | Operating Agency | Frequency
MONTGOMERY | 31.7 | USACE | Hourly
HANNIBAL | 126.4 | Hydropower | Hourly
RACINE | 237.5 | Hydropower | Hourly
KYGER | 260.0 | Electric Utility | Hourly
GREENUP | 341.0 | Hydropower | Hourly
MARKLAND | 531.5 | Hydropower | 15 Min
McALPINE | 606.8 | Hydropower | Hourly
J T MYERS | 846 | ORSANCO | 30 Min
SMITHLAND | 919 | ORSANCO | 30 Min