## Slide 1: 213th Technical Committee Meeting Agenda Item 8: Storm Water Abatement Report (informational item)
Steve Braun
sbraun@orsanco.org

## Slide 2: Status of MS4
At the 2012 Tech meeting ORSANCO began tracking progress of MS4 communities
MS4 – Municipal Separate Storm Sewer Systems
Regulation of Stormwater is Intended to reduce pollutants that are carried to waterways via storm sewers from urbanized areas, Industrial and Construction Activities
Carried out in two Phases
  Phase I
  Phase II

## Slide 3: 6 Minimum Controls
Public Education and Outreach
Public Participation/ Involvement
Illicit Discharge Detection and Elimination
Construction Site Runoff Control
Post-Construction Runoff Control
Pollution Prevention/Good Housekeeping

## Slide 4: Recent News
Nov. 17, 2016
  EPA adopted the federal “MS4 General Permit Remand Rule” for Phase II only
  The old way did not allow a public notice
  The NOI was the functional equivalent of an individual permit
    Establishes two alternative approaches to issue MS4 phase II permits
      Comprehensive General Permit
      Two-Step General Permit
    Will promote greater public participation
    Clarifies what is necessary to “reduce the discharge of pollutants to the maximum extent possible”

## Slide 5: Phase I MS4’s
Began in 1990
Permit needed if:
  Medium to Large Communities serving a population of >100,000
  Industry falls within one of 10 categories
  Construction Sites disturbing more than 5 acres of land
Must have an approved Storm Water Management Plan with 6 minimum controls
Must Conduct analytical Monitoring
Louisville is only Phase I MS4 along Ohio River

## Slide 6: Phase II MS4’s
Began in 1999
Permit needed if:
  Designated a small MS4 in urbanized areas defined by the US Census (>50,000 & Density of 1000 people/sq-mile)
  Construction sites disturbing 1-5 acres of land
Usually a general Permit that can cover multiple nearby MS4 communities (co-permittees)
Have an approved Storm Water Management Plan with 6 minimum controls
Usually does not require monitoring but reduce pollutants to the “Maximum Extent Possible”

## Slide 7: MS4’s along the Ohio River
73 (was 69) Permitted MS4 Communities/Counties – could grow as population grows
Only one Phase I community (Louisville)

## Slide 8: MS4 State Details
Indiana
  16 Permittees
  All in compliance
  No changes in 2015 or 2016
Illinois
  No MS4 Communities
  No changes in 2015 or 2016
Kentucky
  11 permittees, some are co-permittees
  6 Cities are in full compliance
  No Changes in 2016

## Slide 9: MS4 State Details cont.
Ohio
  2 notable changes
  15 Permittees
    14 permittees are in full compliance
    Belmont Co. dissolved into 4 different permits
    Likewise, City of Cincinnati separated from Hamilton Co. and received their own permit
PA
  20 Permittees
  All in Compliance
  No changes from previous year

## Slide 10: MS4 State Details cont.
WV
  11 Permittees
  One city is in full compliance
  Monitoring for TKN, Nitrite, Nitrate, Total Phosphorus and others at main outfall

## Slide 11: Questions? *informational item
Conclusion
Most of the MS4 Communities are in compliance
All Are Working toward full compliance
New remand rule should have little effect on Ohio River MS4’s